Embedded Programming
with the GNU Toolchain
Vijay Kumar B.
vijaykumar@zilogic.com

---
What?
C Application
OS
C Application
Hardware
Hardware
Conventional C Programs
Our Case

---
Why?
Embedded Firmware Development
RTOS development – eCOS, RTEMS, ...
Bootloader development – U-Boot, ...
Programming DSPs
Testing Microprocessors cores implemented in ASICs / FPGAs

---
How?
3 Example Scenarios
Hello Embedded World – Add 2 numbers in registers in assembly
Add 2 numbers from memory in assembly
Add 2 numbers from memory in C

---
Scenario I - Overview
Cortex-M3 Processor
Writing Assembly Programs
Emulating Cortex-M3 with Qemu

---
ARMv7
Latest revision of ARM architecture – ARMv7
Cortex Processor – ARMv7 implementation
Profiles
  - A Profile – GPOS and applications
  - R Profile – optimized for realtime systems
  - M Profile – optimized for low cost embedded systems

---
Cortex-M3 Features
Thumb-2 Instruction Set
Bit Banding
Integrated Peripherals
  - NVIC
  - Memory Protection Unit (MPU)
  - Debug Peripherals

---
CM3 SoCs
SoC vendors license CM3 from ARM
SoC vendors use it as building block
Licensees
  - TI – Stellaris processors
  - Atmel – ATSAM3U series
  - STMicroelectronics – STM32
  - NXP - LPC1700

---
LM3S811
Cortex-M3 core
Memory
  - 64KB Flash
  - 8KB RAM
Peripherals
  - 10 bit ADCs
  - I2C, SPI, UARTs, PWM
  - 32 GPIOs

---
Registers
Load Store Architecture
Data processing instructions – register operands
Large register file – 16 32-bit registers

---
Registers (Contd.)
R0 – R12
  - General Purpose
R13
  - Stack Pointer
R14
  - Link Register
R15
  - Program Counter
R0
R8
R1
R9
R2
R10
R3
R11
R4
R12
R5
R13 (SP)
R6
R14 (LR)
R7
R15 (PC)
PSR
PRIMASK
FAULTMASK
CONTROL
BASEPRI

---
Memory Map
CM3 has a fixed memory map
Easy to port software
4GB Address Space
LM3S811
  - 64KB Flash
  - 8KB SRAM
Peripherals
0x4000_0000
SRAM
0x2000_0000
Flash
0x0000_0000

---
Reset
SP from address 0x0
PC from address 0x4
Address is mapped to Flash
Initial SP
Reset Vec.
0x0000
0x0004

---
Assembly
 label: instruction	@comment
label: convenient way to refer to the memory location
instruction: ARM instruction or assembler directive
comment: starts with @

---
Hello Embedded World
        .thumb
        .syntax unified
sp: .word 0x100
reset: .word start+1
start:
        mov r0, #5
        mov r1, #4
        add r2, r1, r0
stop: b stop

---
Toolchain
Assembler Source (.s)
Assembler (as)
Object File (.o)
Linker (ld)
Executable (.elf)

---
Toolchain (Contd.)
 $ arm-none-eabi-as -mcpu=cortex-m3 -o add.o add.s
Cross toolchain prefix - arm-none-eabi-
-mcpu=cortex-m3 Specifies the CPU
-o Specifies the output file

---
Toolchain (Contd.)
 $ arm-none-eabi-ld -Ttext=0x0 -o add.elf add.o
Cross toolchain prefix - arm-none-eabi-
-Ttext=0x0 Addresses should be assigned to instructions starting from 0.
-o Specifies the output file

---
Toolchain (Contd.)
 $ arm-none-eabi-nm add.elf
 ...
 00000004 t reset
 00000000 t sp
 00000008 t start
 00000014 t stop
List symbols from object file
Verify initial SP and reset vector are located at required address

---
Toolchain (Contd.)
ELF file format contains meta information for OS
Binary format contains consecutive bytes starting from an address
Convenient for flashing tools

---
Toolchain (Contd.)
 $ arm-none-eabi-objcopy -O binary add.elf add.bin
objcopy – converts between different executable file formats
-O specifies that output file format

---
Qemu
Open source machine emulator - the processor and the peripherals
Architectures – i386, ARM, MIPS, SPARC ...
Used by various open source projects
  - OLPC
  - OpenMoko
  - Linux Kernel Testing

---
Emulating in Qemu
 $ qemu-system-arm -M lm3s811evb -kernel add.bin
-M lm3s811evb specifies the machine to be emulated
-kernel specifies data to be loaded in Flash from address 0x0
monitor interface – control and status
can be used to view the registers

---
Review
Writing simple assembly programs
Building and linking them using GNU Toolchain
Emulating Cortex-M3 processor using Qemu

---
Scenario II - Overview
Role of Linker
Linker Scripts
Placing data in RAM

---
Linker
assembler
a.o
a.s
linker
abc.o
assembler
b.s
b.o
assembler
c.o
c.s
In multi-file programs – combines multiple object files to form executable

---
Linker (Contd.)
Linker
Symbol
Resolution
Relocation
Section
Merging
Section
Placement

---
Linker (Contd.)
Linker
Symbol
Resolution
Relocation
Section
Merging
Section
Placement

---
Symbol Resolution
Functions are defined in one file
Referenced in another file
References are marked unresolved by the compiler
Linker patches the references

---
Linker
Linker
Symbol
Resolution
Relocation
Section
Merging
Section
Placement

---
Relocation
Code generated assuming it starts from address X
Code should start from address Y
Change addresses assigned to labels
Patch label references

---
Sections
Placing related bytes at a particular location.
Example:
  - instructions in Flash
  - data in RAM
Related bytes are grouped together using sections
Placement of sections can be specified

---
Sections (Contd.)
Most programs have atleast two sections, .text and .data
Data or instructions can be placed in a section using directives
Directives
  - .text
  - .data
  - .section

---
Sections (Contd.)
Source – sections can be interleaved
Bytes of a section – contiguous addresses

---
Linker
Linker
Symbol
Resolution
Relocation
Section
Merging
Section
Placement

---
Section Merging
Linker merges sections in the input files into sections in the output file
Default merging – sections of same name
Symbols get new addresses, and references are patched
Section merging can be controlled by linker script files

---
Linker
Linker
Symbol
Resolution
Relocation
Section
Merging
Section
Placement

---
Section Placement
Bytes in each section is given addresses starting from 0x0
Labels get addresses relative to the start of section
Linker places section at a particular address
Labels get new address, label references are patched

---
strlen

---
Linker Script
Linker
Symbol
Resolution
Relocation
Can be controlled
through Linker scripts.
Section
Merging
Section
Placement

---
Simple Linker Script
MEMORY {
    FLASH (rx) : ORIGIN = 0x00000000, LENGTH = 0x10000
    SRAM (rwx) : ORIGIN = 0x20000000, LENGTH = 0x2000
}
SECTIONS {
    .text : {
        abc.o (.text);
        def.o (.text);
    } > FLASH
}
0xFFFF
def.o (.text)
abc.o (.text)
0x0

---
Simple Linker Script
MEMORY {
    FLASH (rx) : ORIGIN = 0x00000000, LENGTH = 0x10000
    SRAM (rwx) : ORIGIN = 0x20000000, LENGTH = 0x2000
}
SECTIONS {
    .text : {
        abc.o (.text);
        def.o (.text);
    } > FLASH
}
Section Merging

---
Simple Linker Script
MEMORY {
    FLASH (rx) : ORIGIN = 0x00000000, LENGTH = 0x10000
    SRAM (rwx) : ORIGIN = 0x20000000, LENGTH = 0x2000
}
SECTIONS {
    .text : {
        abc.o (.text);
        def.o (.text);
    } > FLASH
}
Section Placement

---
Making it Generic
MEMORY {
    FLASH (rx) : ORIGIN = 0x00000000, LENGTH = 0x10000
    SRAM (rwx) : ORIGIN = 0x20000000, LENGTH = 0x2000
}
SECTIONS {
    .text : {
        * (.text);
    } > FLASH
}
Wildcards to represent .text
form all input files

---
Multiple Sections
MEMORY {
    FLASH (rx) : ORIGIN = 0x00000000, LENGTH = 0x10000
    SRAM (rwx) : ORIGIN = 0x20000000, LENGTH = 0x2000
}
SECTIONS {
    .text : {
        * (.text);
    } > FLASH
    .rodata : {
        * (.rodata);
    } > FLASH
}
0xFFFF
Dealing with
mutiple sections
.rodata
.text
0x0

---
Data in RAM
Add two numbers from memory
Assembly source
Linker Script

---
RAM is Volatile!
RAM is volatile
Data cannot be made available in RAM at power-up
All code and data should be in Flash at power-up
Startup code – copies data from Flash to RAM

---
RAM is Volatile! (Contd.)
.data section should be present in Flash at power-up
Section has two addresses
  - load address (aka LMA)
  - run-time address (aka VMA)
So far only run-time address – actual address assigned to labels
Load address defaults to run-time address

---
Linker Script Revisited
MEMORY {
    FLASH (rx) : ORIGIN = 0x00000000, LENGTH = 0x10000
    SRAM (rwx) : ORIGIN = 0x20000000, LENGTH = 0x2000
}
SECTIONS {
    .text : {
        * (.text);
    } > FLASH
    .data : {
        * (.data);
    } > SRAM
}
0x20001FFF
SRAM
.data
0x20000000
0x0000FFFF
Flash
.text
0x00000000

---
Linker Script Revisited
MEMORY {
    FLASH (rx) : ORIGIN = 0x00000000, LENGTH = 0x10000
    SRAM (rwx) : ORIGIN = 0x20000000, LENGTH = 0x2000
}
SECTIONS {
    .text : {
        * (.text);
    } > FLASH
    .data : {
        * (.data);
    } > SRAM AT> FLASH
}
0x20001FFF
SRAM
.data
0x20000000
0x0000FFFF
.data
Flash
.text
0x00000000

---
Linker Script Revisited
MEMORY {
    FLASH (rx) : ORIGIN = 0x00000000, LENGTH = 0x10000
    SRAM (rwx) : ORIGIN = 0x20000000, LENGTH = 0x2000
}
SECTIONS {
    .text : {
        * (.text);
        etext = .;
    } > FLASH
    .data : {
        sdata = .;
        * (.data);
        edata = .;
    } > SRAM AT> FLASH
}
edata
.data
sdata
.data
etext
.text

---
Data in RAM
Copy .data from Flash to RAM
start:
        ldr r0, =sdata @ Load the address of sdata
        ldr r1, =edata @ Load the address of edata
        ldr r2, =etext @ Load the address of etext
copy: ldrb r3, [r2] @ Load the value from Flash
        strb r3, [r0] @ Store the value in RAM
        add r2, r2, #1 @ Increment Flash pointer
        add r0, r0, #1 @ Increment RAM pointer
        cmp r0, r1 @ Check if end of data
        bne copy @ Branch if not end of data

---
Review
Linker Script can control
  - Section Merging
  - Section Placement
.data placed in RAM, .text in Flash
RAM is volatile
at load time .data is in Flash
at startup .data is copied from Flash to RAM

---
Scenario III - Overview
C Environment Requirements
C Sections
C Source Code
Linker Script

---
Doing it in C
Environment has to be setup
  - Stack pointer
  - Non-initalized global variables, initialized to zero
  - Initialized global variables must have their initial value

---
C Sections
Sections created by GCC
  - .text – for functions
  - .data – for initialized global data
  - .bss – for uninitialized global data
  - .rodata – for strings and global variables defined as const

---
Credits
Cash Register – Nikola Smolenski
Cerebral Cortex - www.toosmarttostart.samhsa.gov
Reset Button – flattop341 http://www.flickr.com/photos/flattop341/224175619/
Church Relocation – Fletcher6 http://commons.wikimedia.org/wiki/File:Salem_Church_Relocation.JPG
Rope Image - Markus BÃ¤rlocher http://commons.wikimedia.org/wiki/File:Schotstek_links.jpg

---
Further Reading
Embedded Programming using the GNU Toolchain - http://www.bravegnu.org/gnu-eprog/
GNU Linker Manual
GNU Assembler Manual